## Slide 1
Analogue Digital Converter
(ADC)
STEVEN FOONG GHIN YEW

## Slide 2: What is ADC ???
ANALOGUE signal input converted into DIGITAL data.

## Slide 3: How ADC works???
Different level of voltage measured and stored into register.
RED : Conversion
BLUE : Input Analogue Signal

## Slide 4: How ADC works???
When the conversion is done frequently, a long analogue signal will be able to be converted and store into registers.

## Slide 5: What is required to perform ADC???
Generally, ADC required the following information
  Threshold voltage control
  Sample time
  Resolution of conversion
Interrupt are used to represent the conversion

## Slide 6: ADC in STM32F42x (GENERAL)
3 ADC in STM32F42x
There are total of 19 available input channel shared to all three ADC
All 3 ADC have same feature and same number of
  Control Register (CR)
  Status Register (SR)
  Data Register (DR)
NOTE: One ADC is enough to sample all 19 channels

## Slide 7: ADC in STM32F42x (Threshold Voltage)
In STM32, threshold voltage is referred as Vref
If the input analogue signal exceeded the threshold voltage range, the process will be halt.
Therefore, the input signals must between Vref- and Vref+,
  Vref+ as the highest allowable input voltage
  Vref- as the lowest allowable input voltage
The two Vref value will be stored in HTR and LTR register
NOTE: The supplied Vss must be equal to Vref-
NOTE: Vref+ must be higher than 1.8V and lower than Vdd

## Slide 8: ADC in STM32F42x (Threshold Voltage)
To enable the Watchdog to generate interrupt, CR1.AWDIE must be set
  If the input signal exceed the threshold voltage range, an interrupt SR.AWD will be generated. We can then halt the conversion.

## Slide 9: ADC in STM32F42x (Resolution)
  The resolution can be calculate with (Vref+ - Vref-)/(2^number of bits)
Number of bits allowed: 12, 10, 8, 6
  4096
  1024
  256
  64
Eg.
  ADC configured with 8 bit resolution and Vref+ = 3.3V, Vref- = -3.3V
  The voltage resolution = (3.3V – (-3.3V))/(2^8) = 0.0257812V
  This mean there will be a 0.0257812V different at every level

## Slide 10: ADC in STM32F42x (Resolution)

## Slide 11: ADC in STM32F42x (Resolution)
CR1.RES [1:0] will be used to set the resolution of the ADC

## Slide 12: ADC in STM32F42x (SLEEP & AWAKE)
There are two mode for the ADC chip, Sleep Mode and Awake Mode
During Sleep Mode, the chip only consume few micro-A which approximately zero. However, no conversion can be perform during the Sleep Mode
The chip can only perform conversion/conversions during Awake Mode
To wake up the ADC chip from Sleep mode, CR2.ADON bit must be set

## Slide 13: ADC in STM32F42x(FAST & SLOW Conv)
There are two conversion mode allowed which is Fast Conversion Mode and Slow Conversion Mode.
To use Fast Conversion Mode, analogue supplied voltage Vdd in the range of 2.4V and 3.6V
To use Slow Conversion Mode, analogue supplied voltage Vdd must in the range of 1.8V and 3.6V

## Slide 14: ADC in STM32F42x (CHANNEL)
STM32F42x consist of 19 ADC pin
  16 External Input pin
  3 Internal Input pin
There are 16 GPIO pins that can be use as ADC input channel which is ADC_IN0, ADC_IN1, … , ADC_IN14 and ADC_IN15.
These channels can be grouped into Regular Group or Injected Group
Regular Group allow 16 conversion
Injected Group allow 4 conversion

## Slide 15: ADC in STM32F42x (CHANNEL)
SQR1.L[3:0] is use to select the number of conversion in the sequence. The sequence can be arranged in SQR3, SQR2 and SQR1.
The sequence can have repeated channel
Eg. With L = 0010 (3 conversion), the sequence can be
  1st: Convert channel ADC_IN0
  2nd: Convert channel ADC_IN1
  3rd: Convert channel ADC_IN0 again
Same case to Injected group but JSQR.JL[1:0] can only have maximum 4 conversion. Therefore only one JSQR register is needed.

## Slide 16: ADC in STM32F42x (CHANNEL)
No. | Regular Channel sequence | Injected Channel sequence
1 | IN0 | IN16
2 | IN3 | IN15
3 | IN2 | IN14
4 | IN0 | IN13
5 | IN6 | 
6 | IN4 | 
7 | IN0 | 
8 | IN9 | 
9 | IN3 | 
10 | IN0 | 
11 | IN2 | 
12 | IN6 | 
13 | IN0 | 
14 | IN4 | 
15 | IN9 | 
16 | IN0 | 
When CR2.JAUTO is not set
Injected group will have higher priority.
Example
During conversion of a regular group channel, JWSTART is set. The current regular conversion will halt and start the injected channel conversion first.

## Slide 17: ADC in STM32F42x (CHANNEL)
The 3 Internal inputs are
  Temperature sensor
    Is connected to ADC_IN18 in STM32F42x
    It can measure the temperature ranging from -40 to 125 ± 1.5 degree celcius
    However, I recommend to use 6 bit resolution while using the temperature sensor
    This is because (125-(-40))/1.5 = 110 which mean that a resolution with more than 110 level will give an inaccurate result. 8 bit would have a resolution up to 256 already
  Vrefint (ACD_IN17)
  Vbat

## Slide 18: ADC in STM32F42x (CHANNEL)
To ENABLE the internal input channel
  Temperature sensor and Vrefint:
    CCR.TSVREFE have to be set HIGH
  Vbat:
    CCR.VBATE have to be set HIGH

## Slide 19: ADC in STM32F42x (CHANNEL)

## Slide 20: ADC in STM32F42x (Conversion)
To start conversion of regular group, the CR1.SWSTART have to be set whereas CR1.JSWSTART set to start injected group.
After the conversion, an interrupt SR.EOC will be generated to acknowledge the end of conversion.
Therefore, this interrupt must be enable by setting CR1.EOCIE to 1.
Same case to injected group with SR.JEOC and CR1.JEOCIE as its interrupt flag and interrupt enable.

## Slide 21: ADC in STM32F42x (Conversion)
Other than using SWSTART and JSWSTART to start.
ADC can also start a conversion from 16 external triggers
First, set the edge of trigger through the CR2.EXTEN[1:0]
  00 No external trigger
  01 Rising Edge trigger
  10 Falling Edge trigger
  11 Both Edge trigger
Second, set the source of trigger through CR2. EXTSEL[3:0]
  There are 16 available sources of trigger including TMR1, TMR2 …

## Slide 22: ADC in STM32F42x (SAMPLING)
The sampling time can be set to every channel individually with the SMP1 and SMP2 registers
However, the time set is not the actual sampling time because the conversion time have to be include.
12 clock cycle have to be added to obtain the actual time scale.
Eg. A 30MHz clock with sampling time set to 3 cycle (case 000)
  The conversion time will be (3 + 12) cycles = 15cycles
  The time needed would be 0.5 micro-s between each sample

## Slide 23: ADC in STM32F42x (SAMPLING)
It is possible to reduce the actual sampling time with the FAST CONVERSION MODE and the resolution setting.
In FAST CONVERSION MODE and resolution to 12bits. The actual sampling time only have to add extra clock cycle as follow:
  12 bits: Sampling time + 12 clock cycle (no change)
  10 bits: Sampling time + 10 clock cycle (reduced 2 cycle)
  8 bits: Sampling time + 8 clock cycle (reduced 4 cycle)
  6 bits: Sampling time + 6 clock cycle (reduced 6 cycle)

## Slide 24: ADC in STM32F42x (DATA STORAGE)
After the conversion, regular group will store the data in:
  Register DR
Whereas, injected group will store the data in:
  Register JDR1
  Register JDR2
  Register JDR3
  Register JDR4

## Slide 25: ADC in STM32F42x (DATA STORAGE)
From previous slide, it is clear that the regular group only have 1 data register DR.
Must keep track when there are more than 1 regular channel
Therefore, NOT CONVENIENT
By using DMA, the system allow the converted data to be stored directly to the memory allocated in the software.
DMA can be enabled by setting CR2.DMA to HIGH.
NOTE: This DMA setting only allow for single ADC mode

## Slide 26: ADC in STM32F42x (DATA STORAGE)
If DMA is used for multiple ADC, CCR.DMA[1:0] have to be configure.
  00: Multi ADC disabled
  01: ADC1 → ADC2 → ADC3
  10: ADC1 & 2 → ADC3 & 1 → ADC2 & 3 (more than 6 bit)
  11: ADC1 & 2 → ADC3 & 1 → ADC2 & 3 (6bit)

## Slide 27: ADC in STM32F42x (DATA STORAGE)
If DMA is used for multiple ADC, CCR.DMA[1:0] have to be configure.
  00: Multi ADC disabled
  01: ADC1 → ADC2 → ADC3
  10: ADC1 & 2 → ADC3 & 1 → ADC2 & 3 (more than 6 bit)
  11: ADC1 & 2 → ADC3 & 1 → ADC2 & 3 (6bit)

## Slide 28: ADC in STM32F42x (MODE)
Single conversion mode, only 1 conversion is done
  Temperature sensor only need 1 conversion
  CR2.CONT must be cleared
Continuous conversion mode
  The ADC will convert that channel again after it finished
  Meaning that it will keep on convert the channel
  CR2.CONT have to be enabled

## Slide 29: ADC in STM32F42x (MODE)
SCAN mode
  The ADC convert all the channels listed in the sequence and restart the converting all the channels if CONT bit is set.
  CR1.SCAN have to be set in order to be in this mode
  if CR2.EOCS == 0
    EOC is generated after the whole sequence is finished
  Else
    EOC is generated after finishing each channel conversion

## Slide 30: ADC in STM32F42x (MODE)
Discontinuous mode
  CR1.DISCEN[0:0]
    This bit is use to ENABLE the discontinuous mode with set and DISABLE with unset.
  CR2.DISCNUM[2:0]
    This 3 bits use to separate the sequence listed in SQR
    Example.
    The setting is DISCNUM = 011 (4 channel) and DISCEN = 1
    The sequence then wait for the second trigger / setting of SWSTART 2nd time
    NOTE: SWSTART and JSWSTART will auto reset once conversion started
No | Channel
1 | IN0
2 | IN1
3 | IN2
4 | IN3
No | Channel
5 | IN4
6 | IN5
7 | IN2
 | -

## Slide 31: ADC in STM32F42x (ALLIGNMENT)
Generally, there are two alignment
  Right Align
  Left Align

## Slide 32: ADC in STM32F42x (ADC Clock)
After all this, you may found your pin unable to perform ADC as there is no CLOCK.
RCC still have to be configured to allow the ADC feature.
To pre-scale clock (division of clock), CCR.ADCPRE[1:0] have to be configured.
APB2 is the CLOCK for ADC. Therefore, we still have to configure the RCC.APB2ENR to ENABLE APB2
But this is not under ADC because it is under RCC. MUAHAHAHAHAHAHA

## Slide 33
THANK YOU